## Slide 1: Inverse Kinematics and Particles
Grant Smith 40111906
Physics-based Animation

## Slide 2: Inverse Kinematics
Implemented using the CCD method
Angle Limits
Reach Limits
Procedural Animation

## Slide 3: Cyclic Coordinate Descent (CCD)
Simple
Fast
Iterative
Process:
Get the axis of rotation (cross product)
Get the angle to rotate (acos + dot product)
Create a quaternion from the axis and angle
If the quaternion is within the angle limits
  Rotate the link
After this is done for each link, apply the rotation from the root link down to the last child

## Slide 4: Inverse Kinematics Testing
To test the Inverse Kinematics:
Create a point to follow
Rotate that point randomly around every axis (x, y, z)
If it can reach
  It should always work
If it can’t reach
  It doesn’t work

## Slide 5: Collision Detection
Sphere v Sphere
AABB v AABB (Axis Aligned Bounding Box)
OBB v OBB (Orientated Bounding Box)
Line v Line
Sphere v Plane
Other combinations will not be covered since they are mostly derivatives of the above

## Slide 6: Sphere v Sphere
Offset vector from sphereA and sphereB
Take the magnitude of the offset
If the sum of the radii is less than the magnitude
  There is an intersection
If the sum of the radii is less than the magnitude
  No Intersection
r
r
offset
Sphere A
Sphere B

## Slide 7: AABB v AABB
  For each axis: x, y and z
    Check centre[axis] of cubeA – centre[axis] of cubeB is less than
    The sum of the dimension of each cube on that axis
  If the check is true on each axis then there is an intersection
cubeA
cubeB
Centre
(x, y, z)
Dimension
(x, y, z)
Centre
(x, y, z)
Dimension
(x, y, z)

## Slide 8: OBB v OBB
cube0.normals[0],
cube0.normals[1],
cube0.normals[2],
cube1.normals[0],
cube1.normals[1],
cube1.normals[2],
cross(cube0.normals[0], cube1.normals[0]),
cross(cube0.normals[0], cube1.normals[1]),
cross(cube0.normals[0], cube1.normals[2]),
cross(cube0.normals[1], cube1.normals[0]),
cross(cube0.normals[1], cube1.normals[1]),
cross(cube0.normals[1], cube1.normals[2]),
cross(cube0.normals[2], cube1.normals[0]),
cross(cube0.normals[2], cube1.normals[1]),
cross(cube0.normals[2], cube1.normals[2])
normalize(cube1.position - cube0.position)
  Take the 3 normal of two cubes (ignoring normals that are the negative of another)
  Add them to a list called ‘axes’
  Take the cross of each normal from the first cube and each normal from the second cube
  Add them to ‘axes’
  Add the normalized offset of the cubes to the list as well ‘axes’
  Get the corners of both cubes and add them to a list called ‘corners’
Centre
(x, y, z)
Dimension
(x, y, z)
Rotation
(4x4 Matrix)
3 Normals
(x, y, z)

## Slide 9: OBB v OBB (cont.)
For every axis in the ‘axes’ list
  Do a 1D intersection test
  If at any point, the 1D intersection is false, there is no intersection = no collision
If each test returned true, pick the test that returned the lowest overlap and use the axis for that as the collision direction
1D intersection test:
  Take the dot product of the axis against each corner (for both cubes)
  Store the min and max value from the dot product for each cube
  Calculate the longSpan = fmax(max0, max1) - fmin(min0, min1)
  Calculate the sumSpan = max0 - min0 + max1 - min1
  If the long span is less than or equal to the sum span, there is an overlap on the axis

## Slide 10: Sphere v plane
Calculate the distance from the origin
Calculate the distance between the sphere and the plane
If <= 0 then there is an intersection
  The direction of the collision is the plane’s normal
r
Planenormal
Planeposition

## Slide 11: Particle System
Hierarchical:
Manager contains many emitters
Emitters contain many particles
This structure allows for:
Emitters to be easily added and removed
The entire system to be updated with ease
Better management of resources
  (eg textures)

## Slide 12
To reduce time wasted allocating and deallocating memory, each emitter has one list of particles that is not dynamic.
Instead of deallocating particles when they die, they change state, reducing the time wasted.
On creation
  set the life time to an initial value and set the state (Alive).
When the life time is <= 0
  Set the state (Not Alive)
Don’t update or render particles in the ‘Not Alive’ state.
Particles make use of linear dynamics to respond to collision
(managed within the Spatial Partitioning Grid)

## Slide 13: Spatial Partitioning
To improve the performance of the particles and reduce the limitations met (particle quantity), the SP grid was implemented.
SP grid:
Splits the entire scene up into small cubes within one large cube
Collision detection and response managed within cells of the grid
Takes 3D world positions and converts them to 1D array positions
  The 1D positions represent a cell

## Slide 14
Each time a collider is updated:
Collider calls the SP grid, passing itself
The grid uses the collider’s position to determine what cells it covers
Passes the collider to relevant cells
Each cell:
  Checks the collider for collisions with other colliders in that cell
  If there is a collision then the corrective impulses and forces are applied
Debug rendering of the Spatial Partitioning Grid
Blue = collider called the cell but no collision checks
Green = 1 to 5 collision checks

## Slide 15: Rigid Bodies – linear dynamics
Rigid bodies implemented using linear dynamics (no rotation)
Implemented for collision response and for more user interaction
  User controlled rigid body
Collision response using impulses with small corrective forces
Implemented using the collider and SP grid
  Collider manages the integration (using Explicit Eular)
  SP grid manages the calculation of impulses and forces to correct collision

## Slide 16: Rigid Bodies – Integration
Integration using the Explicit Euler method
  Vn+1 = vn + αnΔt <-- Velocity incremented by the acceleration relative to the time passed
  Sn+1 = Sn + VnΔt <-- Position incremented by the velocity relative to the time passed
Acceleration is calculated using Newton’s Second Law
  = ma
  =

## Slide 17: Collision Response
Impulse calculated using:
  Impulse =
  = direction of collision
  = velocity of one collider
  = velocity of other collider
  = elasticity constant
The impulse is applied directly to the collider by the SP grid in order to correct collisions.

## Slide 18: Improvements
Particle System implemented using compute shaders
  Reduce load on cpu by passing it to the gpu
Self colliding Inverse Kinematics
Make the Spatial Partitioning Grid more dynamic
  Adapts to the scene better (cells with different size/shape)